## Slide 1: BPF+
Exploiting Global Data-flow Optimization in a Packet Filter Architecture
Andrew Begel, Steven McCanne, Susan L. Graham
University of California, Berkeley
with acknowledgments to Van Jacobson

## Slide 2: The Big Picture
With BPF+, we can express packet filters in a high-level language and compile them into efficient code.

## Slide 3: The Packet Filter
Definition: A tool for selecting packets from a packet stream using a programmable selection criterion.
Example: tcp and source net 128.32/16 and destination host web.mit.edu and port 80

## Slide 4: Domain-Specific Optimization
Tune traditional compiler optimizations for the application of packet filtering.
Affords simpler analyses and much more effective optimization.
  Packet filters are DAGs
  Engenders linear-time algorithms
Combine with Just-In-Time (JIT) assembly.

## Slide 5
5
10
15
20
25
30
0
500
1000
1500
2000
2500
Number of Table Entries
Filter Time (ns)
BPF+ Linear
BPF+ Hash
Optimized C
Comparison of C Optimizer to BPF+ Optimizer

## Slide 6: Related Work
Virtual Machine Models:
  CMU/Stanford Packet Filter: MRA87
  BPF: Berkeley Packet Filter: MJ93
    tcpdump and libpcap
  MPF: YBMEM94
Exploit Filter Structure:
  PathFinder: BGPP94
  DPF: EK96
  Multi-dimensional Range Matching: LS98
  Grid of Tries: SVSW98
High-Level Approach:
  LR Parsing: JC96

## Slide 9: Compiler Optimizations
Leverage modern compiler technology
Powerful intermediate form
  Static Single Assignment (SSA)
Three key optimizations
  Redundant Predicate Elimination
  Partial Redundancy Elimination
  Lookup Table Encapsulation

## Slide 10: Redundant Predicate Elimination
Packet header parsing leads to many redundant predicates.
Unlike traditional optimizations, detect redundant edges rather than redundant computation.
Packet filter control flow graphs are edge-rich.

## Slide 11: (src host UCB and dest host MIT) or (src host MIT and dest host UCB)
All packets between UCB and MIT

## Slide 15: Partial Redundancy Elimination
Packet header parsing also leads to much redundant computation.

## Slide 16: src host UCB or src host MIT
All packets that come from either UCB or MIT

## Slide 20: Putting Them Both Together
(6 steps later...)
Combining partial redundancy elimination with redundant predicate elimination is much more effective than using either alone.

## Slide 22: Lookup Table Encapsulation
After early optimizations, many predicates reduced to simple field comparisons.
Use analysis to discover opportunities for moving into lookup tables.
Implementation may use linear search, binary search, hash lookup or any combination of the three.

## Slide 23: src host UCB or src host MIT or src host CMU
All packets that come from UCB, MIT or CMU

## Slide 29: Filter Safety Must Be Verified
All bytecodes are valid.
Jump targets are valid.
No loops.
All paths terminate with a return instruction.
No out-of-bounds reads or writes.

## Slide 31: Performance Tests
Two types of predicate expressions
  Dependent (src host (UCB or MIT or CMU)
  Independent (i.e. TCP, Port 80, dest host UCB)
Run on Ultra 10 300 MHz UltraSPARC IIi
Four ways to run a filter
  Unoptimized, Interpreted
  Optimized, Interpreted
  Unoptimized, JIT Assembled
  Optimized, JIT Assembled

## Slide 32
5
10
15
20
25
30
100
150
200
250
300
350
400
450
500
Number of Dependent Table Entries
Filter Time (ns)
BPF+ Linear
BPF+ Hash Table
Comparison of Linear Search to Hash Lookup

## Slide 33
1
2
3
4
5
6
7
8
9
1
0
1
5
2
0
3
0
0
2
0
0
0
4
0
0
0
60
0
0
8
0
0
0
1
0
0
0
0
1
2
0
0
0
N
u
m
b
e
r
o
f
D
e
p
e
n
d
e
n
t
T
a
b
l
e
E
n
t
r
i
e
s
Filter Time (ns)
U
n
o
p
t
i
m
i
z
e
d
I
n
t
e
r
p
r
e
t
e
d
O
p
t
i
m
i
z
e
d
I
n
t
e
r
p
r
e
t
e
d
U
n
o
p
t
i
m
i
z
e
d
A
s
s
e
m
b
l
e
d
O
p
t
i
m
i
z
e
d
A
s
s
e
m
b
l
e
d
Effects of Optimization and JIT Assembly

## Slide 34
5
10
15
20
25
30
100
1000
10000
Number of Dependent Table Entries
Filter Time (ns) (log scale)
Unoptimized Interpreted
Optimized Interpreted
Unoptimized Assembled
Optimized Assembled
Effects of Optimization and JIT Assembly (log scale)

## Slide 35
1
2
3
4
5
100
200
300
400
500
700
1000
2000
4000
Number of Independent Predicates
Filter Time (ns) (log scale)
Unoptimized Interpreted
Optimized Interpreted
Unoptimized Assembled
Optimized Assembled
Effects of Optimization and JIT Assembly
on Independent Predicates (log scale)

## Slide 36: Future Work
More efficient table lookup representations (LS98, SVSW98)
Better support for packet classification
Loops
  Proof-Carrying Code, Necula 96
Intrusion detection
  Online Updates

## Slide 37: Conclusions
Packet filters can be specified at a high-level and be efficiently executed.
Key idea: Tune familiar global data-flow compiler analyses and optimizations for packet filtering.